## Slide 1: Secure Data Export and Auditing using Data Diodes
Douglas W. Jones and Tom C. Bowersox
Department of Computer Science
THE UNIVERSITY OF IOWA
This work was partially supported by NSF Grant CNS-05243 (ACCURATE).
http://www.cs.uiowa.edu/~jones/voting/diode/

## Slide 2: The Problem
Election result must be put on the net.
Election database must be protected.
Conflict resolved by:
  Sneakernet or
  Even odder solutions
Miami Dade County Solution
Security through obscurity

## Slide 3: What we need
A data diode
Allow data export
Prevent data import
Design understood by
  Election observers
  Election officials
  Losing candidates

## Slide 4: US Patent 5,703,562
Claims limited to up-hierarchy transmission
Example given for RS-232 implementation
  Transmit: 1 IC + 8 components + 5 volt supply
  Receive: 1 IC + 4 components + 5 volt supply
Explain this to a naïve suspicious observer!

## Slide 5: Commercial Data Diodes
Both based on fiber-optic technology
Tenix Data Diode certified to EAL 7 under Common Criteria
www.owlcti.com
www.tenix.com

## Slide 6: Design Transparency
EAL 7 certification
  Insufficient if the certifying agency is not trusted
  What if the vendor cheats after certification?
Therefore, we need
  Complete design transparency
  Open documentation
  Rights of observers to inspect entire mechanism
  Minimal complexity

## Slide 7: Our Design
Avoid all black boxes
  no 3-terminal devices
  No ICs
Extreme simplicity
  Use RS-232

## Slide 8: Explaining the circuit board
Must explain function of
  Every circuit trace
  Every component

## Slide 9: Explaining the Transmitter
GND: signal ground
TxD: transmit data
When TxD is positive
  Top LED lights
When TxD is negative
  Bottom LED lights
Resistor needed as
  Current limiter

## Slide 10: Explaining the Transmitter
The shield pin in the cable
  Connects to metallic sheath
The shield pin on the board
  Connects to trace that surrounds the electronics
Together
  These make it difficult to use conductors inside the shield as radio antennas

## Slide 11: Explaining the Transmitter
The loopback connections
  Tell computer we're ready
RTS to CTS
  Request To Send (input)
  Clear To Send (output)
DTR to DSR and DCD
  Data Terminal Ready (input)
  Data Set Ready (output)
  Data Carrier Detect (output)

## Slide 12: Explaining the Receiver
The power supply
  Uses RTS TxD and DTR
Power from Serial cable
Power from special cable
  2 batteries
  AC power from wall outlet
Capacitors and Diodes
  Permit 60Hz operation

## Slide 13: Explaining the Receiver
The Receiver itself
  Uses the power supply
  Transmits to RxD output
Top photodiode
  Pulls RxD positive
Bottom photodiode
  Pulls RxD negative
Resistors needed as
  Current limiters

## Slide 14: Using the Data Diode
No reverse channel (almost)
  Must rely entirely on forward error correction
  Checksums (or better) to reject bad data
  Redundancy to provide for correction
  Operational status determined from downstream
Sending from high to low security domain
  Covert content in data is a big issue
  Unlike most low to high transmission

## Slide 15: Auditors and Wiretaps
Data exported from EMS is public
Observers should not trust the web server
So, observers should be allowed wiretaps
  Directly observe data-flow to server
  Directly verify that data conforms to spec
Free air (as opposed to fiber optic) optical data diodes offer excellent access to the data stream by observers!

## Slide 16: Exporting Election Results
Using relational database terminology
election results are a single relation over:
Precinct (or split, for split precincts)
Race (or contest)
Candidate (or position with respect to contest)
Votes for that candidate in that race in that precinct
What we need to do is export this entire relation

## Slide 17: OASIS EML, A Bad Idea
Requires header
  Data diode invites an infinite stream
Verbose
  human audit difficult
Covert channels
  Complex rules for canonical form
Difficult to checksum
#-- EML-20081104-US-CA-Santa_Clara_County-2216-1274.xml --#
<?xml version="1.0" encoding="UTF-8"?>
<CastVote xmlns="440-castvote.xsd">
<ElectionEvent>
<Event>
<EventName Id="n1274s213">
Santa Clara County, CA, USA (2008-11-04)
</EventName>
<EventQualifier>Precint 2216</EventQualifier>
</Event>
<Election>
<ElectionName>Presidency</ElectionName>
<Contest>
<ContestName>President</ContestName>
<Selection>
<Option>
<OptionName>V. I. Lenin</OptionName>
</Option>
</Selection>
</Contest>
</Election>
<Election>
<ElectionName>Presidency</ElectionName>
<Contest>
<ContestName>Vice-President</ContestName>
<Selection>
<Option>
<OptionName>Karl Marx</OptionName>
</Option>
</Selection>
</Contest>
</Election>
<Election>
<ElectionName>Senate</ElectionName>
<Contest>
<ContestName>Senator</ContestName>
<Selection>
<Option>
<OptionName>William Lloyd Garrison</OptionName>
</Option>

## Slide 18: Reasonable Data Formats
A repeating stream of checksummed records
Tab separated fields?
IC15 President Lincoln 25 16384
CV06 Mayor Thomas 42 32768
XMLish but not really XML
<ITEM PRECINCT=”IC15” RACE=”President” CANDIDATE=”Lincoln” VOTES=”25” />53895
<ITEM PRECINCT=”CV06” RACE=”mayor” CANDIDATE=”Thomas” VOTES=”42” />41274
We opt (on weak grounds) for XMLish

## Slide 19: Covert Channels
The Risk
  Covert export of security keys from EMS
The Defense
  Rigid format constraints on data
    No optional, permutable, or alternate elements
    No free use of whitespace or line ends
  Code audit on real-time checks in transmit code
    No non-constant time delays allowed in transmitter

## Slide 20: Transparent Checksums
We have a transparent data diode design
We have a transparent data format
We need a transparent checksum algorithm
  Understandable using highschool math
  Easy to code in a bad programming language
CRC-16 is not transparent!
  Try explaining this: X16 + X15 + X2 + 1
  Or this:

## Slide 21: Transparent Checksums
A classic transparent but weak checksum
  S0 = 0; Si+1 = (Si + Ci) mod 256
A modest proposal
  S0 = 0; Si+1 = (5Si + Ci) mod 65536
  Akin to multiplicitative congruence PRNG
What multipliers and moduli are best
Is there a cryptographically secure hash code that meets our transparency goals?

## Slide 22: Code to checksum data stream
#include <stdio.h>
/* filter to checksum each block of angle-bracketed text
Reads from stdin and copies to stdout.
Appends decimal checksum to each closing angle bracket.
Angle brackets are included in the checksum.
NOTE: This code is dumb, bracket nesting is ignored and
bracked imbalance is not checked. */
main ()
{
int ch;
unsigned int sum = 0;
while ((ch = getchar()) != EOF) {
putchar( ch );
sum = (sum * 5 + ch) % 66636; /*accumulate*/
if (ch == '<') {
sum = '<'; /*initialize*/
} else if (ch == '>') {
printf("%1u",sum);
} } }
Even this is hard to explain, but it's in reach of a student who only has a semester of programming, perhaps in VB or worse

## Slide 23: A Prototype Application
UNDER CONSTRUCTION
UNDER CONSTRUCTION
UNDER CONSTRUCTION
Scaffolding
  Extract results from example county data
  Inject in model EMS database
Demo code
  Cyclically scan EMS database
  Export through data diode
Decent quality prototype application code
  Receive data from data diode to mirror database
  Server-side web application for results

## Slide 24: Other Applications
Upstream
In voting machine